## Slide 1: Space Radiation 101
Michael J. Pecaut, PhD
Vice Chair & Professor
Division of Biomedical Engineering Sciences (BMES)
Program Director
Neuroscience, Systems Biology & Bioengineering Program (NSBB)
LOMA LINDA UNIVERSITY | Department of Basic Sciences
11175 Campus St., Chan Shun Pavilion, Rm. A-1016, Loma Linda, CA 92354
Phone: 909-558-8372

## Slide 2: Background Radiation Exposure ≈ 0.360 mSv / year (w/o Medical Exposures)
http://www.bbc.co.uk/schools/gcsebitesize/science/add_ocr_gateway/radiation/radioisotopesrev1.shtml
Chest X-ray ~ 0.1 mSv; Mammogram ~ 2.5 mSv; CT Scan ~ 30 – 100 mSv
Space Station Annual Dose ~ 0.1 Sv; A-Bomb Dose ~ 1-4 Sv; RT 20 – 90 Sv
N Metting, DOE Low Dose Program

## Slide 3: Complex Space Radiation Field
Sources Outside and Inside the Solar System
Notes: 3

## Slide 4
Exploring Space In Partnership
Using the International Space Station
Operating in the Lunar Vicinity
2030s
Leaving the Earth-Moon System and Reaching Mars Orbit
Now
2020s
Phase 0
Solve exploration mission challenges through research and systems testing on the ISS. Understand if and when lunar resources are available
Phase 1
Conduct missions in cislunar space; assemble Deep Space Gateway and Deep Space Transport
Phase 2
Complete Deep Space Transport and conduct Mars verification mission
Phases 3 and 4
Missions to the Mars system, the surface of Mars
Advancing technologies, discovery and creating economic opportunities
20 -40 day missions
200 -400 day missions
500 -900 day missions
Notes: Transport Hab will have ~180 m3 of habitable volume (also 280m3 total … with only 180 of it as habitable)
Deep Space Gateway
This first phase of exploration near the moon will use current technologies and allow us to gain experience with extended operations farther from Earth than previously completed. These missions enable NASA to develop new techniques and apply innovative approaches to solving problems in preparation for longer-duration missions far from Earth.
In addition to demonstrating the safe operation of the integrated SLS rocket and Orion spacecraft, the agency is also looking to build a crew tended spaceport in lunar orbit within the first few missions that would serve as a gateway to deep space and the lunar surface. This deep space gateway would have a power bus, a small habitat to extend crew time, docking capability, an airlock, and serviced by logistics modules to enable research. The propulsion system on the gateway mainly uses high power electric propulsion for station keeping and the ability to transfer among a family of orbits in the lunar vicinity. The three primary elements of the gateway, the power and propulsion bus and habitat module, and a small logistics module(s), would take advantage of the cargo capacity of SLS and crewed deep space capability of Orion. An airlock can further augment the capabilities of the gateway and can fly on a subsequent exploration mission, Building the deep space gateway will allow engineers to develop new skills and test new technologies that have evolved since the assembly of the International Space Station. The gateway will be developed, serviced, and utilized in collaboration with commercial and international partners.
“I envision different partners, both international and commercial, contributing to the gateway and using it in a variety of ways with a system that can move to different orbits to enable a variety of missions,” said William Gerstenmaier, associate administrator for Human Exploration and Operations at NASA Headquarters in Washington. “The gateway could move to support robotic or partner missions to the surface of the moon, or to a high lunar orbit to support missions departing from the gateway to other destinations in the solar system.”
Deep Space Transport
The second phase of missions will confirm that the agency’s capabilities built for humans can perform long duration missions beyond the moon. For those destinations farther into the solar system, including Mars, NASA envisions a deep space transport spacecraft. This spacecraft would be a reusable vehicle that uses electric and chemical propulsion and would be specifically designed for crewed missions to destinations such as Mars. The transport would take crew out to their destination, return them back to the gateway, where it can be serviced and sent out again. The transport would take full advantage of the large volumes and mass that can be launched by the SLS rocket, as well as advanced exploration technologies being developed now and demonstrated on the ground and aboard the International Space Station.
This second phase will culminate at the end of the 2020s with a one year crewed mission aboard the transport in the lunar vicinity to validate the readiness of the system to travel beyond the Earth-moon system to Mars and other destinations, and build confidence that long-duration, distant human missions can be safely conducted with independence from Earth. Through the efforts to build this deep space infrastructure, this phase will enable explorers to identify and pioneer innovative solutions to technical and human challenges discovered or engineered in deep space.
To achieve the agency’s goal to extend humanity’s presence in the solar system will require the best research, technologies and capabilities from international partners and the private sector. NASA will look to partners for potential contributions of spaceflight hardware and the delivery of supplemental resources. The gateway and transport could potentially support mission after mission as a hub of activity in deep space near the moon, representing multiple countries and agencies with partners from both government and private industry. NASA is open to new ideas of both a technical and programmatic nature suggestions as we develop, mature and implement this plan.
.

## Slide 5: Geomagnetic Field and Trapped Radiation Belts

## Slide 6: Earth’s Magnetosphere

## Slide 7: Van Allen Radiation belts

## Slide 8
Solar Particle Events

## Slide 9: There Are Two Main Types of SPEs Impulsive vs Gradual
R Turner
Notes: Solar proton events are generally observed in association with solar x-ray flux increases. The x-ray flux is seen as either a very rapid rise to peak maximum flux and subsequent rapid decay [impulsive], or rapid rise followed by a gradual decrease [gradual]. The impulsive x-ray signature is associated with a solar flare, while the longer x-ray signature is associated with the eruption of a Coronal Mass Ejection.
There are significant differences between the two classes of SPEs:
Impulsive SPEs are generally short-lived, with much lower peak flux and total fluence, acting over a relatively low range of solar longitudes. Gradual SPEs are the greater risk to astronauts, with potentially a much larger peak flux and total fluence, acting over a much larger range of solar longitudes.

## Slide 10: Coronal Mass Ejections (Gradual Events)
Bubble of gas and magnetic field
Ejects ~1017 g of matter
Shock wave accelerates particles enroute to 3000 km/s vs 400 km/s for solar wind
Reaches Earth after ~ 1 day
Associated with magnetic storms
Proton rich solar events 10x worse than flares
Notes: 10

## Slide 11: Solar Flare (Impulsive Event)
Particles arrive at Earth within minutes if field lines aligned.
Energy of particles is determined by events at Sun atmosphere

## Slide 12: Solar Particle Events
Increased levels of protons and heavier ions
Energies
  Protons 100s of MeV
  Heavier ions - 100s of GeV
Abundances depend on radial distance from Sun
Partially ionized species have greater ability to penetrate magnetosphere
Generally unpredictable
  Frequency a function of solar cycle
Notes: 12

## Slide 13: Cyclical Variation of Solar Activity
X-ray
View
Sunspot
Number
Corona
Structure
Notes: 13

## Slide 14: Probability Varies with Solar Cycle
>30 MeV
Smoothed Sunspot Number
>10 MeV
R Turner, ANSER, Inc.
Oct 89
Solar Particle Events by Fluence Since 1955
(with Smoothed Sunspot Number)
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
Year
Event Fluence (Protons/cm
2
)
0
50
100
150
200
250
10
6
10
7
10
8
10
9
10
10
10
11
Smoothed Sunspot Number
Aug 72
Solar Particle Events by Fluence Since 1955
(with Smoothed Sunspot Number)
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
Year
Event Fluence (Protons/cm
)
0
50
100
150
200
250
10
6
10
7
10
8
10
9
10
10
10
11
Smoothed Sunspot Number
Jul, Nov 00
Notes: 14
Solar Particle Events are roughly correlated with the 10-to-11-year solar cycle, occurring more frequently during seven years of high solar activity than the three or so years near solar minimum. Each solar cycle has its own character with 10 to 30 large events (> 108 protons/cm2 with energy greater than 10 MeV) per cycle. However, the intensity of the event is not correlated with the sun-spot cycle, with several large events (Aug 72 and the not-shown Oct/Nov 04) occurring late in the declining phase of the cycle.

## Slide 15
Galactic Cosmic Rays

## Slide 16: GCR Abundance vs Ionizing Power

## Slide 17: Cosmic Ray Tracks from Apollo 8 Track DensityVaries with Z2
Schaefer & Sullivan, 1976
Notes: 17
Ilford emulsion tracks from H.J. Schaefer & J.J. Sullivan, 1976.
Atlas of Nuclear Emulsion Micrographs from Personnel Dosimeters of Manned Space Missions. Naval Aerospace Medical Research Laboratory, Pensacola, FL. Monograph 22
Fig 14.

## Slide 18: NASA’s Risks and Risk Limits

## Slide 19
Space Safety Requirements
Congress has chartered the National Council on Radiation Protection (NCRP) to guide Federal agencies on radiation limits and procedures
  NCRP guides NASA on astronaut dose limits
Crew safety
  limit of 3% fatal cancer risk
  prevent radiation sickness during mission
  new exploration requirements limit brain and heart disease risks from space radiation
Mission and Vehicle Requirements
  shielding, dosimetry, and countermeasures
NASA programs must follow the ALARA principle to ensure astronauts do not approach dose limits

## Slide 20: The Fundamental Concept of Dose is Misleading
Dose is defined as energy absorbed per unit mass (irrespective of the spatial distribution of the absorbed energy)
Low LET radiation deposits
energy in a uniform pattern
1 Dose Unit
High LET radiation deposits
energy in a non-uniform pattern
1 Dose Unit
Notes: 20
The concept of dose, a macroscopic parameter, can be misleading when applied to microscopic patterns of energy deposition. At a given exposure it is less likely that a small target will be “hit” by a charged particle than a field of photons, but when it occurs, the energy deposition is large.

## Slide 21: The Biology Is Even More Complicated
Dose Responses Are Not All Linear
  U-Shaped
Particle Effects May Be Unique
  Effects may trend oppositely
  Quality factors very hard to define
Mixed Particle Exposures May Not Produce Simple Additive Responses
Sequential Exposures Don’t Produce Simple Additive Responses
Dose Rate Effects Unclear for Particles
  What are the biological time constants?

## Slide 22: Important Questions
Central Nervous System
  How does radiation impact the CNS (e.g. behavior, cognitive function, neurodegenerative disease)?
Retina
  What role does radiation play in spaceflight-induced deficits in vision?
Heart & Vasculature
  Does space radiation have a significant impact on cardiovascular health?

## Slide 23: Important Questions
Microbiomes
  How does chronic exposure to the space radiation environment impact astronaut microbiome and ISS microbe ecology?
Communication between Physiological Systems -
  How does radiation impact sympathetic nervous system control of other physiological systems (e.g. immune, cardiopulmonary, musculoskeletal)?
  What happens to the radiation environment at the interface between hard and soft tissues (e.g. bone-bone marrow, skull-brain-vasculature, biofilms)?

## Slide 24: Important Questions
Synergy with other Space Environment Factors
  How does space radiation effects interact with those of microgravity, vibration, high CO2, circadian rhythm, etc.?
Timing
  What are the immediate vs. late effects of radiation?
Energy
  How do biological effects differ across different radiation types and energies?
  How do the biological effects of the space radiation environment differ between low earth orbit and deep space?

## Slide 25
Thank You!

## Slide 26
Doses in Context: Powers of Ten
A-bomb
ISS
Annual